## Slide 1
ESP32 General Purpose Input Output
Yogesh M Iggalore

## Slide 2
GPIO | Input | Output | Functions | Board | Notes
GPIO00 | Pulled up | OK | ADC2_CH1, TOUCH1, RTC_GPIO11 | DTR pin pulled high | Output PWM signal at boot
GPIO01 | UART0 TX | OK | UART0 TX pin | UART0 TX pin | Debug output pin at boot
GPIO02 | OK | OK | ADC2_CH2, TOUCH2, RTC_GPIO12 | GREEN LED | Connected to GREEN led
GPIO03 | OK | UART0 RX | UART0 RX | UART0 RX | High at boot
GPIO04 | OK | OK | ADC2_CH0, TOUCH0, RTC_GPIO10 | RED LED | Connected to RED LED
GPIO05 | OK | OK | VSPI CS0 | SPI_CS sd card | SD card chip select
GPIO12 | OK | OK | ADC2_CH5, TOUCH5, HSPI_MISO, RTC_GPIO15 | TOUCH-2 | Boot fail if pulled high
GPIO13 | OK | OK | ADC2_CH4, TOUCH4, HSPI_MOSI, RTC_GPIO14 | BLUE LED | Connected to blue led
GPIO14 | OK | OK | ADC2_CH6, TOUCH6, HSPI_CLK, RTC_GPIO16 | TOUCH-3 | Output PWM signal at boot
GPIO15 | OK | OK | VSPI_CS0 | TOUCH-1 | Touch input 1
GPIO16 | OK | OK | UART2 RX | COMM_RX | UART communication RX pin

## Slide 3
GPIO | Input | Output | Functions | Micro | Notes
GPIO17 | OK | OK | UART2 TX | COMM_TX | UART communication TX pin
GPIO18 | OK | OK | VSPI_CLK | SPI_CLK | SD card clock pin
GPIO19 | OK | OK | VSPI_MISO | SPI_MISO | SD card miso pin
GPIO21 | OK | OK | I2C_SDA | I2C_SDA | I2C sda pin
GPIO22 | OK | OK | I2C_SCL | I2C_SCL | I2C scl pin
GPIO23 | OK | OK | VSPI_MOSI | SPI_MOSI | SD card mosi pin
GPIO25 | OK | OK | ADC2_CH8, DAC1, RTC_GPIO06 | Relay | Connected to relay control
GPIO26 | OK | OK | ADC2_CH9, DAC2, RTC_GPIO07 | SPI_Extra | External SPI chip select
GPIO27 | OK | OK | ADC2_CH7,TOUCH-7, RTC_GPIO17 | TOUCH-4 | Touch input 4
GPIO32 | OK | OK | ADC1_CH4,TOUCH-9, RTC_GPIO09 | ADC/POT | Analog pins
GPIO33 | OK | OK | ADC1_CH5,TOUCH-8, RTC_GPIO08 | DHT | Dht sensor
GPIO34 | OK | - | ADC1_CH7, RTC_GPIO05 | Switch-1 | INPUT Only
GPIO35 | OK | - | ADC1_CH7, RTC_GPIO05 | Switch-2 | INPUT Only
GPIO36 | OK | - | ADC1_CH0, Sensor_VP, RTC_GPIO00 | Switch-3 | INPUT Only
GPIO39 | OK | - | ADC1_CH0, Sensor_VN, RTC_GPIO03 | Switch-4 | INPUT Only

## Slide 4: Drive Mode: Strong and Slow Strong
Strong Drive Mode
Slow Strong Drive Mode
Normal output mode. Works like an inverter.
Rise/Fall times 12ns Max
Controlled rise/fall times. Rise/Fall times 60 ns Max.
Saves power
GND
VCC
From MCU
core
Port Pin
To MCU Input Logic
GND
VCC
Port Pin
To MCU Input Logic
From MCU Core

## Slide 5: Drive Mode: Open Drain - Drives High/Low
Open Drain-Drives high
Connect a resistor externally from pin to ground
VCC
From MCU Core
Port Pin
To MCU Input Logic
GND
From MCU Core
Port Pin
To MCU Input Logic
Open Drain-Drives Low
Connect a resistor externally from pin to Vdd

## Slide 6: Drive Mode: Hi-Z and Analog Hi-Z
Hi-Z Mode
Digital Input Mode
GND
VCC
Port Pin
To MCU Digital Input Logic
Analog Hi-Z Mode
Analog Input Mode.
Select when port is unused since it consumes no power.
GND
VCC
Port Pin
To MCU Analog Input Logic

## Slide 7: Drive Mode: Resistive Pull-Up and Pull-Down
Resistive Pull-Up
Effective Circuit if written with ‘1’
VCC
Port Pin
To MCU Input Logic
5.6K
Port Pin
To MCU Input Logic
5.6K
Resistive Pull-Down
Effective Circuit if written with ‘0’
NOTE: If you are using this mode as input-only, make sure to write correct value to port!
GND
VCC
Port Pin
To MCU Input Logic
5.6K
From MCU Core
GND
VCC
Port Pin
To MCU Input Logic
5.6K
From MCU Core

## Slide 8: Example: Switches and Pushbutton Inputs
5.6K
VCC
Button
SPST Button: Produces either Vcc or Floating input.
Adding a pull-down resistor fixes it.
Port Pin
To MCU Input Logic
5.6K
VCC
Button
MCU port in Pull-Down mode
Don’t Forget: Write ‘0’ to port

## Slide 10
GPIO API
void pinMode(uint8_t pin, uint8_t mode)
Description | This function to start serial module
Parameter | Baudrate, serial config
Return | Void
Example | Serial.begin(9600, SERIAL_8N1); // starts UART0 with baudrate 9600 parity none and stopbit 1
void end();
Description | This function to stops serial module
Parameter | void
Return | Void
Example | Serial.end(); // stops UART0